## Slide 1: Floating Point
COE 301 / ICS 233
Computer Organization
Dr. Muhamed Mudawar
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Floating-Point Numbers
The IEEE 754 Floating-Point Standard
Floating-Point Comparison, Addition and Subtraction
Floating-Point Multiplication
MIPS Floating-Point Instructions and Examples

## Slide 3: The World is Not Just Integers
Programming languages support numbers with fraction
  Called floating-point numbers
  Examples:
  3.14159265… (π)
  2.71828… (e)
  1.0 × 10–9 (seconds in a nanosecond)
  8.64 × 1013 (nanoseconds in a day)
  The last number is a large integer that cannot fit in a 32-bit register
We use a scientific notation to represent
  Very small numbers (e.g. 1.0 × 10–9)
  Very large numbers (e.g. 8.64 × 1013)
  Scientific notation: ± d . fraction × 10 ± exponent

## Slide 4: Floating-Point Numbers
Examples of floating-point numbers in base 10
  -5.341×103 , 2.013×10–1
Examples of floating-point numbers in base 2
  -1.00101×223 , 1.101101×2–3
  Exponents are kept in decimal for clarity
Floating-point numbers should be normalized
  Exactly one non-zero digit should appear before the point
    In a decimal number, this digit can be from 1 to 9
    In a binary number, this digit should be 1
  Normalized: -5.341×103 and 1.101101×2–3
  NOT Normalized: -0.05341×105 and 1101.101×2–6
decimal point
binary point

## Slide 5: Floating-Point Representation
A floating-point number is represented by the triple
  Sign bit (0 is positive and 1 is negative)
    Representation is called sign and magnitude
  Exponent field (signed value)
    Very large numbers have large positive exponents
    Very small close-to-zero numbers have negative exponents
    More bits in exponent field increases range of values
  Fraction field (fraction after binary point)
    More bits in fraction field improves the precision of FP numbers
S
Exponent
Fraction

## Slide 6: IEEE 754 Floating-Point Standard
Found in virtually every computer invented since 1980
  Simplified porting of floating-point numbers
  Unified the development of floating-point algorithms
  Increased the accuracy of floating-point numbers
Single Precision Floating Point Numbers (32 bits)
  1-bit sign + 8-bit exponent + 23-bit fraction
Double Precision Floating Point Numbers (64 bits)
  1-bit sign + 11-bit exponent + 52-bit fraction
S
Exponent8
Fraction23
S
Exponent11
Fraction52
(continued)

## Slide 7: Normalized Floating Point Numbers
For a normalized floating point number (S, E, F)
Significand is equal to (1.F)2 = (1.f1f2f3f4…)2
  IEEE 754 assumes hidden 1. (not stored) for normalized numbers
  Significand is 1 bit longer than fraction
Value of a Normalized Floating Point Number:
 (1.F)2 × 2exponent_value
 (1.f1f2f3f4 …)2 × 2exponent_value
 (1 + f1×2-1 + f2×2-2 + f3×2-3 + f4×2-4 …)2 × 2exponent_value
S = 0 is positive, S = 1 is negative
S
E
F = f1 f2 f3 f4 …

## Slide 8: Biased Exponent Representation
How to represent a signed exponent? Choices are …
  Sign + magnitude representation for the exponent
  Two’s complement representation
  Biased representation
IEEE 754 uses biased representation for the exponent
  Exponent Value = E – Bias (Bias is a constant)
The exponent field is 8 bits for single precision
  E can be in the range 0 to 255
  E = 0 and E = 255 are reserved for special use (discussed later)
  E = 1 to 254 are used for normalized floating point numbers
  Bias = 127 (half of 254)
  Exponent value = E – 127 Range: -126 to +127

## Slide 9: Biased Exponent – Cont’d
For double precision, the exponent field is 11 bits
  E can be in the range 0 to 2047
  E = 0 and E = 2047 are reserved for special use
  E = 1 to 2046 are used for normalized floating point numbers
  Bias = 1023 (half of 2046)
  Exponent value = E – 1023 Range: -1022 to +1023
Value of a Normalized Floating Point Number is
 (1.F)2 × 2(E-Bias)
 (1.f1f2f3f4 …)2 × 2(E-Bias)
 (1 + f1×2-1 + f2×2-2 + f3×2-3 + f4×2-4 …)2 × 2(E-Bias)
S = 0 is positive, S = 1 is negative

## Slide 10: Examples of Single Precision Float
What is the decimal value of this Single Precision float?
Solution:
  Sign = 1 is negative
  E = (01111100)2 = 124, E – bias = 124 – 127 = –3
  Significand = (1.0100 … 0)2 = 1 + 2-2 = 1.25 (1. is implicit)
  Value in decimal = –1.25 × 2–3 = –0.15625
What is the decimal value of?
Solution:
  Value in decimal = +(1.01001100 … 0)2 × 2130–127 =
  (1.01001100 … 0)2 × 23 = (1010.01100 … 0)2 = 10.375
1
0
1
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
1
0
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
implicit

## Slide 11: Examples of Double Precision Float
What is the decimal value of this Double Precision float ?
Solution:
  Value of exponent = (10000000101)2 – Bias = 1029 – 1023 = 6
  Value of double = (1.00101010 … 0)2 × 26 (1. is implicit) =
  (1001010.10 … 0)2 = 74.5
What is the decimal value of ?
Do it yourself! (answer should be –1.5 × 2–7 = –0.01171875)
0
1
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 12: Decimal to Binary Floating-Point
Convert –0.8125 to single and double-precision floating-point
Solution:
  Fraction bits can be obtained using multiplication by 2
    0.8125 × 2 = 1.625
    0.625 × 2 = 1.25
    0.25 × 2 = 0.5
    0.5 × 2 = 1.0
    Stop when fractional part is 0, or after computing all required fraction bits
  Fraction = (0.1101)2 = (1.101)2 × 2 –1 (Normalized)
  Exponent = –1 + Bias = 126 (single precision) and 1022 (double)
0.8125 = (0.1101)2 = ½ + ¼ + 1/16 = 13/16
1
0
1
1
1
1
1
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
1
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Single Precision
Double Precision

## Slide 13: Largest Normalized Float
What is the Largest normalized float?
Solution for Single Precision:
  E – bias = 254 – 127 = +127 (largest exponent for SP)
  Significand = (1.111 … 1)2 = 1.99999988 = almost 2
  Value in decimal ≈ 2 × 2+127 ≈ 2+128 ≈ 3.4028 … × 10+38
Solution for Double Precision:
  Value in decimal ≈ 2 × 2+1023 ≈ 2+1024 ≈ 1.79769 … × 10+308
Overflow: exponent is too large to fit in the exponent field
0
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 14: Smallest Normalized Float
What is the smallest (in absolute value) normalized float?
Solution for Single Precision:
  Exponent – bias = 1 – 127 = -126 (smallest exponent for SP)
  Significand = (1.000 … 0)2 = 1
  Value in decimal = 1 × 2-126 = 1.17549 … × 10-38
Solution for Double Precision:
  Value in decimal = 1 × 2-1022 = 2.22507 … × 10-308
Underflow: exponent is too small to fit in exponent field
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 15: Zero, Infinity, and NaN
Zero
  Exponent field E = 0 and fraction F = 0
  +0 and -0 are both possible according to sign bit S
Infinity
  Infinity is a special value represented with maximum E and F = 0
    For single precision with 8-bit exponent: maximum E = 255
    For double precision with 11-bit exponent: maximum E = 2047
  Infinity can result from overflow or division by zero
  +∞ and -∞ are both possible according to sign bit S
NaN (Not a Number)
  NaN is a special value represented with maximum E and F ≠ 0
  0 / 0  NaN, 0 ×   NaN, sqrt(-1)  NaN
  Operation on a NaN is typically a NaN: Op(X, NaN)  NaN

## Slide 16: Denormalized Numbers
IEEE standard uses denormalized numbers to …
  Fill the gap between 0 and the smallest normalized float
  Provide gradual underflow to zero
Denormalized: exponent field E is 0 and fraction F ≠ 0
  The Implicit 1. before the fraction now becomes 0. (denormalized)
Value of denormalized number ( S, 0, F )
Single precision:  (0.F)2 × 2-126
Double precision:  (0.F)2 × 2-1022
Denorm
Denorm
+∞
Positive
Overflow
-∞
Negative
Overflow
Negative
Underflow
Positive
Underflow
Normalized (–ve)
Normalized (+ve)
2–126
2128
0
-2128
-2–126

## Slide 17: Summary of IEEE 754 Encoding
Single-Precision | Exponent = 8 | Fraction = 23 | Value
Normalized Number | 1 to 254 | Anything | ± (1.F)2 × 2E – 127
Denormalized Number | 0 | nonzero | ± (0.F)2 × 2–126
Zero | 0 | 0 | ± 0
Infinity | 255 | 0 | ± ∞
NaN | 255 | nonzero | NaN
Double-Precision | Exponent = 11 | Fraction = 52 | Value
Normalized Number | 1 to 2046 | Anything | ± (1.F)2 × 2E – 1023
Denormalized Number | 0 | nonzero | ± (0.F)2 × 2–1022
Zero | 0 | 0 | ± 0
Infinity | 2047 | 0 | ± ∞
NaN | 2047 | nonzero | NaN

## Slide 18: Next . . .
Floating-Point Numbers
The IEEE 754 Floating-Point Standard
Floating-Point Comparison, Addition and Subtraction
Floating-Point Multiplication
MIPS Floating-Point Instructions and Examples

## Slide 19: Floating-Point Comparison
IEEE 754 floating point numbers are ordered (except NaN)
  Because the exponent uses a biased representation …
    Exponent value and its binary representation have same ordering
  Placing exponent before the fraction field orders the magnitude
    Larger exponent  larger magnitude
    For equal exponents, Larger fraction  larger magnitude
    0 < (0.F)2 × 2Emin < (1.F)2 × 2E–Bias < ∞ (Emin = 1 – Bias)
  Sign bit provides a quick test for signed <
Integer comparator can compare the magnitudes
Integer
Magnitude
Comparator
X < Y
X == Y
X > Y
X = (EX , FX)
Y = (EY , FY)

## Slide 20: Floating Point Addition
Consider Adding Single-Precision Floats:
1.111001000000000000000102 × 24
+ 1.100000000000001100001012 × 22
Cannot add significands … Why?
  Because exponents are not equal
How to make exponents equal?
  Shift the significand of the lesser exponent right
  Difference between the two exponents = 4 – 2 = 2
  So, shift right second number by 2 bits and increment exponent
1.100000000000001100001012 × 22
= 0.01100000000000001100001 012 × 24

## Slide 21: Floating-Point Addition – cont'd
Now, ADD the Significands:
1.11100100000000000000010 × 24
+ 1.10000000000000110000101 × 22
1.11100100000000000000010 × 24
+ 0.01100000000000001100001 01 × 24 (shift right)
10.01000100000000001100011 01 × 24 (result)
Addition produces a carry bit, result is NOT normalized
Normalize Result (shift right and increment exponent):
10.01000100000000001100011 01 × 24
= 1.00100010000000000110001 101 × 25 (normalized)

## Slide 22: Rounding
Single-precision requires only 23 fraction bits
However, Normalized result can contain additional bits
1.00100010000000000110001 | 1 01 × 25
Two extra bits are used for rounding
  Round bit: appears just after the normalized result
  Sticky bit: appears after the round bit (OR of all additional bits)
Since RS = 11, increment fraction to round to nearest
1.00100010000000000110001 × 25
+1
1.00100010000000000110010 × 25 (Rounded)
Round Bit: R = 1
Sticky Bit: S = 1

## Slide 23: Floating-Point Subtraction
Addition is used when operands have the same sign
Addition becomes a subtraction when sign bits are different
Consider adding floating-point numbers with different signs:
+ 1.00000000101100010001101 × 2-6
– 1.00000000000000010011010 × 2-1
+ 0.00001000000001011000100 01101 × 2-1 (shift right 5 bits)
– 1.00000000000000010011010 × 2-1
0 0.00001000000001011000100 01101 × 2-1
1 0.11111111111111101100110 × 2-1 (2's complement)
1 1.00001000000001000101010 01101 × 2-1 (Negative result)
– 0.11110111111110111010101 10011 × 2-1 (Sign Magnitude)
2's complement of result is required if result is negative

## Slide 24: Floating-Point Subtraction – cont'd
+ 1.00000000101100010001101 × 2-6
– 1.00000000000000010011010 × 2-1
– 0.11110111111110111010101 10011 × 2-1 (Sign Magnitude)
Result should be normalized (unless it is equal to zero)
  For subtraction, we can have leading zeros. To normalize, count the number of leading zeros, then shift result left and decrement the exponent accordingly.
– 0.11110111111110111010101 1 0011 × 2-1
– 1.11101111111101110101011 0011 × 2-2 (Normalized)
Guard bit
Guard bit: guards against loss of a fraction bit
  Needed for subtraction only, when result has a leading zero and should be normalized.

## Slide 25: Floating-Point Subtraction – cont'd
Next, the normalized result should be rounded
– 0.11110111111110111010101 1 0 011 × 2-1
– 1.11101111111101110101011 0 011 × 2-2 (Normalized)
Guard bit
Round bit: R=0
Sticky bit: S = 1
Since R = 0, it is more accurate to truncate the result even though S = 1. We simply discard the extra bits.
– 1.11101111111101110101011 0 011 × 2-2 (Normalized)
– 1.11101111111101110101011 × 2-2 (Rounded to nearest)
IEEE 754 Representation of Result
1
0
1
1
1
1
1
0
1
1
1
1
0
1
1
1
1
1
1
1
1
0
1
1
1
0
1
0
1
0
1
1

## Slide 26: Rounding to Nearest Even
Normalized result has the form: 1. f1 f2 … fl R S
  The round bit R appears immediately after the last fraction bit fl
  The sticky bit S is the OR of all remaining additional bits
Round to Nearest Even: default rounding mode
Four cases for RS:
  RS = 00  Result is Exact, no need for rounding
  RS = 01  Truncate result by discarding RS
  RS = 11  Increment result: ADD 1 to last fraction bit
  RS = 10  Tie Case (either truncate or increment result)
    Check Last fraction bit fl (f23 for single-precision or f52 for double)
    If fl is 0 then truncate result to keep fraction even
    If fl is 1 then increment result to make fraction even

## Slide 27: Additional Rounding Modes
IEEE 754 standard includes other rounding modes:
Round to Nearest Even: described in previous slide
Round toward +Infinity: result is rounded up
  Increment result if sign is positive and R or S = 1
Round toward -Infinity: result is rounded down
  Increment result if sign is negative and R or S = 1
Round toward 0: always truncate result
Rounding or Incrementing result might generate a carry
  This occurs only when all fraction bits are 1
  Re-Normalize after Rounding step is required only in this case

## Slide 28: Example on Rounding
Round following result using IEEE 754 rounding modes:
–1.11111111111111111111111 1 0 × 2-7
Round to Nearest Even:
  Increment result since RS = 10 and f23 = 1
  Incremented result: –10.00000000000000000000000 × 2-7
  Renormalize and increment exponent (because of carry)
  Final rounded result: –1.00000000000000000000000 × 2-6
Round towards +∞:
  Truncated Result: –1.11111111111111111111111 × 2-7
Round towards –∞:
  Final rounded result: –1.00000000000000000000000 × 2-6
Round towards 0:
Round Bit
Sticky Bit
Truncate result since negative
Increment since negative and R = 1
Truncate always

## Slide 29: Accuracy can be a Big Problem
Value1 | Value2 | Value3 | Value4 | Sum
1.0E+30 | -1.0E+30 | 9.5 | -2.3 | 7.2
1.0E+30 | 9.5 | -1.0E+30 | -2.3 | -2.3
1.0E+30 | 9.5 | -2.3 | -1.0E+30 | 0
Adding double-precision floating-point numbers (Excel)
Floating-Point addition is NOT associative
Produces different sums for the same data values
Rounding errors when the difference in exponent is large

## Slide 30: Floating Point Addition / Subtraction
1. Compare the exponents of the two numbers. Shift the smaller number to the right until its exponent would match the larger exponent.
2. Add / Subtract the significands according to the sign bits.
3. Normalize the sum, either shifting right and incrementing the exponent or shifting left and decrementing the exponent.
4. Round the significand to the appropriate number of bits, and renormalize if rounding generates a carry.
Start
Done
Overflow or
underflow?
Exception
yes
no
Shift significand right by
d = | EX – EY |
Add significands when signs
of X and Y are identical,
Subtract when different.
Convert negative result from 2's complement to sign-magnitude.
Normalization shifts right by 1 if there is a carry, or shifts left by the number of leading zeros in the case of subtraction.
Rounding either truncates fraction, or adds a 1 to least significant fraction bit.

## Slide 31: Floating Point Adder Block Diagram
c
z
EZ
EX
FX
Shift Right / Left
Inc / Dec
EY
Swap
FY
Shift Right
Exponent
Subtractor
Significand
Adder/Subtractor
1
1
sign
Sign
Computation
d = | EX – EY |
max ( EX , EY )
add / subtract
Rounding Logic
sign
SY
add/sub
FZ
SZ
c
SX
z
Detect carry, or
Count leading 0’s
c
0 1

## Slide 32: Next . . .
Floating-Point Numbers
The IEEE 754 Floating-Point Standard
Floating-Point Comparison, Addition and Subtraction
Floating-Point Multiplication
MIPS Floating-Point Instructions and Examples

## Slide 33: Floating Point Multiplication Example
Consider multiplying:
-1.110 1000 0100 0000 1010 00012 × 2–4
× 1.100 0000 0001 0000 0000 00002 × 2–2
Unlike addition, we add the exponents of the operands
  Result exponent value = (–4) + (–2) = –6
Using the biased representation: EZ = EX + EY – Bias
  EX = (–4) + 127 = 123 (Bias = 127 for single precision)
  EY = (–2) + 127 = 125
  EZ = 123 + 125 – 127 = 121 (exponent value = –6)
Sign bit of product can be computed independently
Sign bit of product = SignX XOR SignY = 1 (negative)

## Slide 34: Floating-Point Multiplication, cont'd
Now multiply the significands:
(Multiplicand) 1.11010000100000010100001
(Multiplier) × 1.10000000001000000000000
111010000100000010100001
111010000100000010100001
1.11010000100000010100001
10.1011100011111011111100110010100001000000000000
24 bits × 24 bits  48 bits (double number of bits)
Multiplicand × 0 = 0 Zero rows are eliminated
Multiplicand × 1 = Multiplicand (shifted left)

## Slide 35: Floating-Point Multiplication, cont'd
Normalize Product:
-10.101110001111101111110011001... × 2-6
Shift right and increment exponent because of carry bit
= -1.010111000111110111111001100... × 2-5
Round to Nearest Even: (keep only 23 fraction bits)
-1.01011100011111011111100 | 1 100... × 2-5
Round bit = 1, Sticky bit = 1, so increment fraction
Final result = -1.01011100011111011111101 × 2-5
IEEE 754 Representation
1
0
1
1
1
1
0
1
0
0
1
0
1
1
1
0
0
0
1
1
1
1
1
0
1
1
1
1
1
1
0
1

## Slide 36: Floating Point Multiplication
1. Add the biased exponents of the two numbers, subtracting the bias from the sum to get the new biased exponent
Multiply the significands. Set the result sign to positive if operands have same sign, and negative otherwise
3. Normalize the product if necessary, shifting its significand right and incrementing the exponent
4. Round the significand to the appropriate number of bits, and renormalize if rounding generates a carry
Start
Done
Overflow or
underflow?
Exception
yes
no
Biased Exponent Addition
EZ = EX + EY – Bias
Result sign SZ = SX xor SY can be computed independently
Since the operand significands 1.FX and 1.FY are ≥ 1 and < 2, their product is ≥ 1 and < 4.
To normalize product, we need to shift right at most by 1 bit and increment exponent
Rounding either truncates fraction, or adds a 1 to least significant fraction bit

## Slide 37: Extra Bits to Maintain Precision
Floating-point numbers are approximations for …
  Real numbers that they cannot represent
Infinite real numbers exist between 1.0 and 2.0
  However, exactly 223 fractions represented in Single Precision
  Exactly 252 fractions can be represented in Double Precision
Extra bits are generated in intermediate results when …
  Shifting and adding/subtracting a p-bit significand
  Multiplying two p-bit significands (product is 2p bits)
But when packing result fraction, extra bits are discarded
Few extra bits are needed: guard, round, and sticky bits
Minimize hardware but without compromising accuracy

## Slide 38: Advantages of IEEE 754 Standard
Used predominantly by the industry
Encoding of exponent and fraction simplifies comparison
  Integer comparator used to compare magnitude of FP numbers
Includes special exceptional values: NaN and ±∞
  Special rules are used such as:
    0/0 is NaN, sqrt(–1) is NaN, 1/0 is ∞, and 1/∞ is 0
  Computation may continue in the face of exceptional conditions
Denormalized numbers to fill the gap
  Between smallest normalized number 1.0 × 2Emin and zero
  Denormalized numbers , values 0.F × 2Emin , are closer to zero
  Gradual underflow to zero

## Slide 39: Floating Point Complexities
Operations are somewhat more complicated
In addition to overflow we can have underflow
Accuracy can be a big problem
  Extra bits to maintain precision: guard, round, and sticky
  Four rounding modes
  Division by zero yields Infinity
  Zero divide by zero yields Not-a-Number
  Other complexities
Implementing the standard can be tricky
Not using the standard can be even worse

## Slide 40: Next . . .
Floating-Point Numbers
The IEEE 754 Floating-Point Standard
Floating-Point Comparison, Addition and Subtraction
Floating-Point Multiplication
MIPS Floating-Point Instructions and Examples

## Slide 41: MIPS Floating Point Coprocessor
Called Coprocessor 1 or the Floating Point Unit (FPU)
32 separate floating point registers: $f0, $f1, …, $f31
FP registers are 32 bits for single precision numbers
Even-odd register pair form a double precision register
Use the even number for double precision registers
  $f0, $f2, $f4, …, $f30 are used for double precision
Separate FP instructions for single/double precision
  Single precision: add.s, sub.s, mul.s, div.s (.s extension)
  Double precision: add.d, sub.d, mul.d, div.d (.d extension)
FP instructions are more complex than the integer ones
  Take more cycles to execute

## Slide 42: Floating-Point Arithmetic Instructions
Instruction | Meaning | Op6 | fmt5 | ft5 | fs5 | fd5 | func6
add.s $f5,$f3,$f4 | $f5 = $f3 + $f4 | 0x11 | 0x10 | $f4 | $f3 | $f5 | 0
sub.s $f5,$f3,$f4 | $f5 = $f3 – $f4 | 0x11 | 0x10 | $f4 | $f3 | $f5 | 1
mul.s $f5,$f3,$f4 | $f5 = $f3 × $f4 | 0x11 | 0x10 | $f4 | $f3 | $f5 | 2
div.s $f5,$f3,$f4 | $f5 = $f3 / $f4 | 0x11 | 0x10 | $f4 | $f3 | $f5 | 3
sqrt.s $f5,$f3 | $f5 = sqrt($f3) | 0x11 | 0x10 | 0 | $f3 | $f5 | 4
abs.s $f5,$f3 | $f5 = abs($f3) | 0x11 | 0x10 | 0 | $f3 | $f5 | 5
neg.s $f5,$f3 | $f5 = –($f3) | 0x11 | 0x10 | 0 | $f3 | $f5 | 7
add.d $f6,$f2,$f4 | $f6,7 = $f2,3 + $f4,5 | 0x11 | 0x11 | $f4 | $f2 | $f6 | 0
sub.d $f6,$f2,$f4 | $f6,7 = $f2,3 – $f4,5 | 0x11 | 0x11 | $f4 | $f2 | $f6 | 1
mul.d $f6,$f2,$f4 | $f6,7 = $f2,3 × $f4,5 | 0x11 | 0x11 | $f4 | $f2 | $f6 | 2
div.d $f6,$f2,$f4 | $f6,7 = $f2,3 / $f4,5 | 0x11 | 0x11 | $f4 | $f2 | $f6 | 3
sqrt.d $f6,$f2 | $f6,7 = sqrt($f2,3) | 0x11 | 0x11 | 0 | $f2 | $f6 | 4
abs.d $f6,$f2 | $f6,7 = abs($f2,3) | 0x11 | 0x11 | 0 | $f2 | $f6 | 5
neg.d $f6,$f2 | $f6,7 = –($f2,3) | 0x11 | 0x11 | 0 | $f2 | $f6 | 7

## Slide 43: Floating-Point Load and Store
Separate floating-point load and store instructions
  lwc1: load word coprocessor 1
  ldc1: load double coprocessor 1
  swc1: store word coprocessor 1
  sdc1: store double coprocessor 1
General purpose register is used as the address register
Instruction | Meaning | Op6 | rs5 | ft5 | Immediate16
lwc1 $f2, 8($t0) | $f2 4 Mem[$t0+8] | 0x31 | $t0 | $f2 | 8
swc1 $f2, 8($t0) | $f2 4 Mem[$t0+8] | 0x39 | $t0 | $f2 | 8
ldc1 $f2, 8($t0) | $f2,3 8 Mem[$t0+8] | 0x35 | $t0 | $f2 | 8
sdc1 $f2, 8($t0) | $f2,3 8 Mem[$t0+8] | 0x3d | $t0 | $f2 | 8

## Slide 44: Data Movement Instructions
Moving data between general purpose and FP registers
  mfc1: move from coprocessor 1 (to a general purpose register)
  mtc1: move to coprocessor 1 (from a general purpose register)
Moving data between FP registers
  mov.s: move single precision float
  mov.d: move double precision float = even/odd pair of registers
Instruction | Meaning | Op6 | fmt5 | rt5 | fs5 | fd5 | func
mfc1 $t0, $f2 | $t0 = $f2 | 0x11 | 0 | $t0 | $f2 | 0 | 0
mtc1 $t0, $f2 | $f2 = $t0 | 0x11 | 4 | $t0 | $f2 | 0 | 0
mov.s $f4, $f2 | $f4 = $f2 | 0x11 | 0x10 | 0 | $f2 | $f4 | 6
mov.d $f4, $f2 | $f4,5 = $f2,3 | 0x11 | 0x11 | 0 | $f2 | $f4 | 6

## Slide 45: Convert Instructions
Convert instruction: cvt.x.y
  Convert the source format y into destination format x
Supported Formats:
  Single-precision float = .s
  Double-precision float = .d
  Signed integer word = .w (in a floating-point register)
Instruction | Meaning | Op6 | fmt5 |  | fs5 | fd5 | func
cvt.s.w $f2,$f4 | $f2 = W2S($f4) | 0x11 | 0x14 | 0 | $f4 | $f2 | 0x20
cvt.s.d $f2,$f4 | $f2 = D2P($f4,5) | 0x11 | 0x11 | 0 | $f4 | $f2 | 0x20
cvt.d.w $f2,$f4 | $f2,3 = W2D($f4) | 0x11 | 0x14 | 0 | $f4 | $f2 | 0x21
cvt.d.s $f2,$f4 | $f2,3 = S2D($f4) | 0x11 | 0x10 | 0 | $f4 | $f2 | 0x21
cvt.w.s $f2,$f4 | $f2 = S2W($f4) | 0x11 | 0x10 | 0 | $f4 | $f2 | 0x24
cvt.w.d $f2,$f4 | $f2 = D2W($f4,5) | 0x11 | 0x11 | 0 | $f4 | $f2 | 0x24

## Slide 46: Floating-Point Compare and Branch
Floating-Point unit has eight condition code cc flags
  Set to 0 (false) or 1 (true) by any comparison instruction
Three comparisons: eq (equal), lt (less than), le (less or equal)
Two branch instructions based on the condition flag
Instruction | Meaning | Op6 | fmt5 | ft5 | fs5 |  | func
c.eq.s cc $f2,$f4 | cc = ($f2 == $f4) | 0x11 | 0x10 | $f4 | $f2 | cc | 0x32
c.eq.d cc $f2,$f4 | cc = ($f2,3 == $f4,5) | 0x11 | 0x11 | $f4 | $f2 | cc | 0x32
c.lt.s cc $f2,$f4 | cc = ($f2 < $f4) | 0x11 | 0x10 | $f4 | $f2 | cc | 0x3c
c.lt.d cc $f2,$f4 | cc = ($f2,3 < $f4,5) | 0x11 | 0x11 | $f4 | $f2 | cc | 0x3c
c.le.s cc $f2,$f4 | cc = ($f2 <= $f4) | 0x11 | 0x10 | $f4 | $f2 | cc | 0x3e
c.le.d cc $f2,$f4 | cc = ($f2,3 <= $f4,5) | 0x11 | 0x11 | $f4 | $f2 | cc | 0x3e
bc1f cc Label | branch if (cc == 0) | 0x11 | 8 | cc,0 | 16-bit Offset |  | 
bc1t cc Label | branch if (cc == 1) | 0x11 | 8 | cc,1 | 16-bit Offset |  | 

## Slide 47: Example 1: Area of a Circle
.data
pi: .double 3.1415926535897924
msg: .asciiz "Circle Area = "
.text
main:
ldc1 $f2, pi # $f2,3 = pi
li $v0, 7 # read double (radius)
syscall # $f0,1 = radius
mul.d $f12, $f0, $f0 # $f12,13 = radius*radius
mul.d $f12, $f2, $f12 # $f12,13 = area
la $a0, msg
li $v0, 4 # print string (msg)
syscall
li $v0, 3 # print double (area)
syscall # print $f12,13

## Slide 48: Example 2: Matrix Multiplication
void mm (int n, float X[n][n], Y[n][n], Z[n][n]) {
for (int i=0; i!=n; i=i+1) {
for (int j=0; j!=n; j=j+1) {
float sum = 0.0;
for (int k=0; k!=n; k=k+1) {
sum = sum + Y[i][k] * Z[k][j];
}
X[i][j] = sum;
}
}
}
Matrix size is passed in $a0 = n
Matrix addresses in $a1 = &X, $a2 = &Y, and $a3 = &Z
What is the MIPS assembly code for the procedure?

## Slide 49: Access Pattern for Matrix Multiply
×
=
X[i][j]
Y[i][k]
Z[k][j]
Matrix X is accessed by row.
Matrix Y is accessed by row.
Matrix Z accessed by column.
&X[i][j] = &X + (i*n + j)*4 = &X[i][j-1] + 4
&Y[i][k] = &Y + (i*n + k)*4 = &Y[i][k-1] + 4
&Z[k][j] = &Z + (k*n + j)*4 = &Z[k-1][j] + 4*n

## Slide 50: Matrix Multiplication Procedure (1 of 3)
# arguments $a0=n, $a1=&X, $a2=&Y, $a3=&Z
mm: sll $t0, $a0, 2 # $t0 = n*4 (row size)
li $t1, 0 # $t1 = i = 0
# Outer for (i = . . . ) loop starts here
L1: li $t2, 0 # $t2 = j = 0
# Middle for (j = . . . ) loop starts here
L2: li $t3, 0 # $t3 = k = 0
move $t4, $a2 # $t4 = &Y[i][0]
sll $t5, $t2, 2 # $t5 = j*4
addu $t5, $a3, $t5 # $t5 = &Z[0][j]
mtc1 $zero, $f0 # $f0 = sum = 0.0

## Slide 51: Matrix Multiplication Procedure (2 of 3)
# Inner for (k = . . . ) loop starts here
# $t3 = k, $t4 = &Y[i][k], $t5 = &Z[k][j]
L3: lwc1 $f1, 0($t4) # load $f1 = Y[i][k]
lwc1 $f2, 0($t5) # load $f2 = Z[k][j]
mul.s $f3, $f1, $f2 # $f3 = Y[i][k]*Z[k][j]
add.s $f0, $f0, $f3 # sum = sum + $f3
addiu $t3, $t3, 1 # k = k + 1
addiu $t4, $t4, 4 # $t4 = &Y[i][k]
addu $t5, $t5, $t0 # $t5 = &Z[k][j]
bne $t3, $a0, L3 # loop back if (k != n)
# End of inner for loop

## Slide 52: Matrix Multiplication Procedure (3 of 3)
swc1 $f0, 0($a1) # store X[i][j] = sum
addiu $a1, $a1, 4 # $a1 = &X[i][j]
addiu $t2, $t2, 1 # j = j + 1
bne $t2, $a0, L2 # loop L2 if (j != n)
# End of middle for loop
addu $a2, $a2, $t0 # $a2 = &Y[i][0]
addiu $t1, $t1, 1 # i = i + 1
bne $t1, $a0, L1 # loop L1 if (i != n)
# End of outer for loop
jr $ra # return to caller