## Slide 1: Performance
COE 301 / ICS 233
Computer Organization
Dr. Muhamed Mudawar
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: What is Performance?
How can we make intelligent choices about computers?
Why is some computer hardware performs better at some programs, but performs less at other programs?
How do we measure the performance of a computer?
What factors are hardware related? software related?
How does machine’s instruction set affect performance?
Understanding performance is key to understanding underlying organizational motivation

## Slide 3: Response Time and Throughput
Response Time
  Time between start and completion of a task, as observed by end user
  Response Time = CPU Time + Waiting Time (I/O, OS scheduling, etc.)
Throughput
  Number of tasks the machine can run in a given period of time
Decreasing execution time improves throughput
  Example: using a faster version of a processor
  Less time to run a task  more tasks can be executed
Increasing throughput can also improve response time
  Example: increasing number of processors in a multiprocessor
  More tasks can be executed in parallel
  Execution time of individual sequential tasks is not changed
  But less waiting time in scheduling queue reduces response time
Notes: Have them raise their hands when answering questions

## Slide 4: Higher Performance = Less Execution Time
For some program running on machine X
X is n times faster than Y
Execution timeX
1
PerformanceX =
PerformanceY
PerformanceX
Execution timeX
Execution timeY
= n
=

## Slide 5: What do we mean by Execution Time?
Real Elapsed Time
  Counts everything:
    Waiting time, Input/output, disk access, OS scheduling, … etc.
  Useful number, but often not good for comparison purposes
Our Focus: CPU Execution Time
  Time spent while executing the program instructions
  Doesn't count the waiting time for I/O or OS scheduling
  Can be measured in seconds, or
  Can be related to number of CPU clock cycles
CPU Execution Time = CPU cycles × Cycle time
Clock rate
CPU cycles
=

## Slide 6: What is the Clock Cycle?
Clock Cycle = Clock period
  Duration between two consecutive rising edges of the clock signal
Clock rate = Clock frequency = 1 / Clock Cycle
  1 Hz = 1 cycle/sec 1 KHz = 103 cycles/sec
  1 MHz = 106 cycles/sec 1 GHz = 109 cycles/sec
  2 GHz clock has a cycle time = 1/(2×109) = 0.5 nanosecond (ns)
Clock
Data transfer & Computation
Update state
Clock Cycle
Clock Cycle 1
Clock Cycle 2
Clock Cycle 3
Operation of digital hardware is governed by a clock

## Slide 7: Improving Performance
To improve performance, we need to
  Reduce the number of clock cycles required by a program, or
  Reduce the clock cycle time (increase the clock rate)
Example:
  A program runs in 10 seconds on computer X with 2 GHz clock
  What is the number of CPU cycles on computer X ?
  We want to design computer Y to run same program in 6 seconds
  But computer Y requires 10% more cycles to execute program
  What is the clock rate for computer Y ?
Solution:
  CPU cycles on computer X = 10 sec × 2 × 109 cycles/s = 20 × 109 cycles
  CPU cycles on computer Y = 1.1 × 20 × 109 = 22 × 109 cycles
  Clock rate for computer Y = 22 × 109 cycles / 6 sec = 3.67 GHz

## Slide 8: Clock Cycles per Instruction (CPI)
Instructions take different number of cycles to execute
  Multiplication takes more time than addition
  Floating point operations take longer than integer ones
  Accessing memory takes more time than accessing registers
CPI is an average number of clock cycles per instruction
Important point
Changing the cycle time often changes the number of cycles required for various instructions
1
I1
cycles
I2
I3
I6
I4
I5
I7
2
3
4
5
6
7
8
9
10
11
12
13
14
CPI =
14/7 = 2.0

## Slide 9: Performance Equation
To execute, a given program will require …
  Some number of machine instructions
  Some number of clock cycles
  Some number of seconds
We can relate CPU clock cycles to instruction count
Performance Equation: (related to instruction count)
CPU cycles = Instruction Count × CPI
CPU Execution Time = Instruction Count × CPI × Cycle time

## Slide 10: Understanding Performance Equation
 | I-Count | CPI | Cycle
Program | X |  | 
Compiler | X | X | 
ISA | X | X | 
Organization |  | X | X
Technology |  |  | X
Execution Time = Instruction Count × CPI × Cycle time

## Slide 11: Using the Performance Equation
Suppose we have two implementations of the same ISA
For a given program
  Machine A has a clock cycle time of 250 ps and a CPI of 2.0
  Machine B has a clock cycle time of 500 ps and a CPI of 1.2
  Which machine is faster for this program, and by how much?
Solution:
  Both computer execute same count of instructions = I
  CPU execution time (A) = I × 2.0 × 250 ps = 500 × I ps
  CPU execution time (B) = I × 1.2 × 500 ps = 600 × I ps
  Computer A is faster than B by a factor = = 1.2
600 × I
500 × I

## Slide 12: Determining the CPI
Different types of instructions have different CPI
Let CPIi = clocks per instruction for class i of instructions
Let Ci = instruction count for class i of instructions
Designers often obtain CPI by a detailed simulation
Hardware counters are also used for operational CPUs
CPU cycles = (CPIi × Ci)
i = 1
n
∑
CPI =
(CPIi × Ci)
i = 1
n
∑
i = 1
n
∑
Ci

## Slide 13: Example on Determining the CPI
Problem
A compiler designer is trying to decide between two code sequences for a particular machine. Based on the hardware implementation, there are three different classes of instructions: class A, class B, and class C, and they require one, two, and three cycles per instruction, respectively.
The first code sequence has 5 instructions: 2 of A, 1 of B, and 2 of C
The second sequence has 6 instructions: 4 of A, 1 of B, and 1 of C
Compute the CPU cycles for each sequence. Which sequence is faster?
What is the CPI for each sequence?
Solution
CPU cycles (1st sequence) = (2×1) + (1×2) + (2×3) = 2+2+6 = 10 cycles
CPU cycles (2nd sequence) = (4×1) + (1×2) + (1×3) = 4+2+3 = 9 cycles
Second sequence is faster, even though it executes one extra instruction
CPI (1st sequence) = 10/5 = 2 CPI (2nd sequence) = 9/6 = 1.5

## Slide 14: Second Example on CPI
Given: instruction mix of a program on a RISC processor
What is average CPI?
What is the percent of time used by each instruction class?
Classi Freqi CPIi
ALU 50% 1
Load 20% 5
Store 10% 3
Branch 20% 2
How faster would the machine be if load time is 2 cycles?
What if two ALU instructions could be executed at once?
CPIi × Freqi
0.5×1 = 0.5
0.2×5 = 1.0
0.1×3 = 0.3
0.2×2 = 0.4
%Time
0.5/2.2 = 23%
1.0/2.2 = 45%
0.3/2.2 = 14%
0.4/2.2 = 18%
Average CPI = 0.5+1.0+0.3+0.4 = 2.2

## Slide 15: MIPS as a Performance Measure
MIPS: Millions Instructions Per Second
Sometimes used as performance metric
  Faster machine  larger MIPS
MIPS specifies instruction execution rate
We can also relate execution time to MIPS
Instruction Count
Execution Time × 106
Clock Rate
CPI × 106
MIPS =
=
Inst Count
MIPS × 106
Inst Count × CPI
Clock Rate
Execution Time =
=
Notes: Book page 61 has an example to show that a machine with a bigger MIPS performance worse than a machine with a smaller MIPS

## Slide 16: Drawbacks of MIPS
Three problems using MIPS as a performance metric
Does not take into account the capability of instructions
  Cannot use MIPS to compare computers with different instruction sets because the instruction count will differ
MIPS varies between programs on the same computer
  A computer cannot have a single MIPS rating for all programs
MIPS can vary inversely with performance
  A higher MIPS rating does not always mean better performance
  Example in next slide shows this anomalous behavior

## Slide 17: MIPS example
Two different compilers are being tested on the same program for a 4 GHz machine with three different classes of instructions: Class A, Class B, and Class C, which require 1, 2, and 3 cycles, respectively.
The instruction count produced by the first compiler is 5 billion Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
The second compiler produces 10 billion Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
Which compiler produces a higher MIPS?
Which compiler produces a better execution time?

## Slide 18: Solution to MIPS Example
First, we find the CPU cycles for both compilers
  CPU cycles (compiler 1) = (5×1 + 1×2 + 1×3)×109 = 10×109
  CPU cycles (compiler 2) = (10×1 + 1×2 + 1×3)×109 = 15×109
Next, we find the execution time for both compilers
  Execution time (compiler 1) = 10×109 cycles / 4×109 Hz = 2.5 sec
  Execution time (compiler 2) = 15×109 cycles / 4×109 Hz = 3.75 sec
Compiler1 generates faster program (less execution time)
Now, we compute MIPS rate for both compilers
  MIPS = Instruction Count / (Execution Time × 106)
  MIPS (compiler 1) = (5+1+1) × 109 / (2.5 × 106) = 2800
  MIPS (compiler 2) = (10+1+1) × 109 / (3.75 × 106) = 3200
So, code from compiler 2 has a higher MIPS rating !!!

## Slide 19: Amdahl’s Law
Amdahl's Law is a measure of Speedup
  How a program performs after improving portion of a computer
  Relative to how it performed previously
Let f = Fraction of the computation time that is enhanced
Let s = Speedup factor of the enhancement only
Speedupoverall = =
Execution Time new
Execution Time old
((1 – f ) + f / s)
1
Fraction f of old time to be enhanced
1 – f
f / s of old time
Execution Time old
Execution Time new
1 – f

## Slide 20: Example on Amdahl's Law
Suppose a program runs in 100 seconds on a machine, with multiply responsible for 80 seconds of this time. How much do we have to improve the speed of multiplication if we want the program to run 4 times faster?
Solution: suppose we improve multiplication by a factor s
25 sec (4 times faster) = 80 sec / s + 20 sec
s = 80 / (25 – 20) = 80 / 5 = 16
Improve the speed of multiplication by s = 16 times
How about making the program 5 times faster?
20 sec ( 5 times faster) = 80 sec / s + 20 sec
s = 80 / (20 – 20) = ∞ Impossible to make 5 times faster!

## Slide 21: Example 2 on Amdahl's Law
Suppose that floating-point square root is responsible for 20% of the execution time of a graphics benchmark and ALL FP instructions are responsible for 60%
One proposal is to speedup FP SQRT by a factor of 10
Alternative choice: make ALL FP instructions 2X faster, which choice is better?
Answer:
  Choice 1: Improve FP SQRT by a factor of 10
  Speedup (FP SQRT) = 1/(0.8 + 0.2/10) = 1.22
  Choice 2: Improve ALL FP instructions by a factor of 2
  Speedup = 1/(0.4 + 0.6/2) = 1.43  Better

## Slide 22: Benchmarks
Performance is measured by running real applications
  Use programs typical of expected workload
  Representatives of expected classes of applications
  Examples: compilers, editors, scientific applications, graphics, ...
SPEC (System Performance Evaluation Corporation)
  Website: www.spec.org
  Various benchmarks for CPU performance, graphics, high-performance computing, Web servers, etc.
  Specifies rules for running list of programs and reporting results
  Valuable indicator of performance and compiler technology
  SPEC CPU 2006 (12 integer + 17 FP programs)

## Slide 23: SPEC CPU Benchmarks
Wall clock time is used as a performance metric
Benchmarks measure CPU time, because of little I/O

## Slide 24: Summarizing Performance Results
Choice of the Reference computer is irrelevant

## Slide 25: Execution Times & SPEC Ratios
Benchmark | Ultra 5 Time (sec) | Opteron Time (sec) | SpecRatio Opteron | Itanium2 Time (sec) | SpecRatio Itanium2 | Opteron/ Itanium2 Times | Itanium2/ Opteron SpecRatios
wupwise | 1600 | 51.5 | 31.06 | 56.1 | 28.53 | 0.92 | 0.92
swim | 3100 | 125.0 | 24.73 | 70.7 | 43.85 | 1.77 | 1.77
mgrid | 1800 | 98.0 | 18.37 | 65.8 | 27.36 | 1.49 | 1.49
applu | 2100 | 94.0 | 22.34 | 50.9 | 41.25 | 1.85 | 1.85
mesa | 1400 | 64.6 | 21.69 | 108.0 | 12.99 | 0.60 | 0.60
galgel | 2900 | 86.4 | 33.57 | 40.0 | 72.47 | 2.16 | 2.16
art | 2600 | 92.4 | 28.13 | 21.0 | 123.67 | 4.40 | 4.40
equake | 1300 | 72.6 | 17.92 | 36.3 | 35.78 | 2.00 | 2.00
facerec | 1900 | 73.6 | 25.80 | 86.9 | 21.86 | 0.85 | 0.85
ammp | 2200 | 136.0 | 16.14 | 132.0 | 16.63 | 1.03 | 1.03
lucas | 2000 | 88.8 | 22.52 | 107.0 | 18.76 | 0.83 | 0.83
fma3d | 2100 | 120.0 | 17.48 | 131.0 | 16.09 | 0.92 | 0.92
sixtrack | 1100 | 123.0 | 8.95 | 68.8 | 15.99 | 1.79 | 1.79
apsi | 2600 | 150.0 | 17.36 | 231.0 | 11.27 | 0.65 | 0.65
Geometric Mean |  |  | 20.86 |  | 27.12 | 1.30 | 1.30
Geometric mean of ratios = 1.30 = Ratio of Geometric means = 27.12 / 20.86

## Slide 26: Things to Remember about Performance
Two common measures: Response Time and Throughput
  Response Time = duration of a single task
  Throughput is a rate = Number of tasks per duration of time
CPU Execution Time = Instruction Count × CPI × Cycle
MIPS = Millions of Instructions Per Second (is a rate)
  FLOPS = Floating-point Operations Per Second
Amdahl's Law is a measure of speedup
  When improving a fraction of the execution time
Benchmarks: real applications are used
  To compare the performance of computer systems
  Geometric mean of SPEC ratios (for a set of applications)

## Slide 27: Performance and Power
Power is a key limitation
  Battery capacity has improved only slightly over time
Need to design power-efficient processors
Reduce power by
  Reducing frequency
  Reducing voltage
  Putting components to sleep
Performance per Watt: FLOPS per Watt
  Defined as performance divided by power consumption
  Important metric for energy-efficiency

## Slide 28: Power in Integrated Circuits
Power is the biggest challenge facing computer design
  Power should be brought in and distributed around the chip
  Hundreds of pins and multiple layers just for power and ground
  Power is dissipated as heat and must be removed
In CMOS IC technology, dynamic power is consumed when switching transistors on and off
Dynamic Power = Capacitive Load × Voltage2 × Frequency
× 40
5V  1V
× 1000

## Slide 29: Trends in Clock Rates and Power
Power Wall: Cannot Increase the Clock Rate
  Heat must be dissipated from a 1.5 × 1.5 cm chip
  Intel 80386 (1985) consumed about 2 Watts
  Intel Core i7 running at 3.3 GHz consumes 130 Watts
  This is the limit of what can be cooled by air

## Slide 30: Example on Power Consumption
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
Relate the Power consumption of the new and old CPUs
Answer:
The Power Wall
  We cannot reduce voltage further
  We cannot remove more heat from the integrated circuit
How else can we improve performance?

## Slide 31: Moving to Multicores
Moving to
Multicore

## Slide 32: Processor Performance
~35000X improvement in processor performance between 1978 and 2012
Performance is slowed down to 22% / year due to power consumption and memory latency
Move to multicore

## Slide 33: Multicore Processors
Multiprocessor on a single chip
Requires explicit parallel programming
Harder than sequential programming
  Parallel programming to achieve higher performance
  Optimizing communication and synchronization
  Load Balancing
In addition, each core supports instruction-level parallelism
  Parallelism at the instruction level
  Parallelism is extracted by the hardware or the compiler
  Each core executes multiple instructions each cycle
  This type of parallelism is hidden from the programmer