## Slide 1: Memory Hierarchy and Caches
COE 301 / ICS 233
Computer Organization
Dr. Muhamed Mudawar
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Random Access Memory and its Structure
Memory Hierarchy and the need for Cache Memory
The Basics of Caches
Cache Performance and Memory Stall Cycles
Improving Cache Performance
Multilevel Caches

## Slide 3: Memory Technology
Static RAM (SRAM)
  Used typically to implement Cache memory
  Requires 6 transistors per bit
  Low power to retain bit
Dynamic RAM (DRAM)
  Used typically to implement Main Memory
  One transistor + capacitor per bit
  Must be re-written after being read
  Must be refreshed periodically
    By reading and rewriting all the rows in the DRAM

## Slide 4: Static RAM Storage Cell
Static RAM (SRAM) Memory
Typically used for caches
Provides fast access time
Cell Implementation:
  6-Transistor cell
  Cross-coupled inverters store bit
  Two pass transistors
  Row decoder selects the word line
  Pass transistors enable the cell to be read and written
Typical SRAM cell
Vcc
Word line
bit
bit
Word line
bit
bit

## Slide 5: Dynamic RAM Storage Cell
Dynamic RAM (DRAM): cheap, dense, but slower than SRAM
Typical choice for main memory
Cell Implementation:
  1-Transistor cell (pass transistor)
  Trench capacitor (stores bit)
Bit is stored as a charge on capacitor
Must be refreshed periodically
  Because of leakage of charge from tiny capacitor
Refreshing for all memory rows
  Reading each row and writing it back to restore the charge
Typical DRAM cell
Word line
bit
Capacitor
Pass
Transistor
Notes: Let’s summarize today’s lecture. The first thing we covered is the principle of locality.
There are two types of locality: temporal, or locality of time and spatial, locality of space.
We talked about memory system design.
The key idea of memory system design is to present the user with as much memory as possible in the cheapest technology while by taking advantage of the principle of locality, create an illusion that the average access time is close to that of the fastest technology.
As far as Random Access technology is concerned, we concentrate on 2: DRAM and SRAM.
DRAM is slow but cheap and dense so is a good choice for presenting the use with a BIG memory system.
SRAM, on the other hand, is fast but it is also expensive both in terms of cost and power, so it is a good choice for providing the user with a fast access time.
I have already showed you how DRAMs are used to construct the main memory for the SPARCstation 20.
On Friday, we will talk about caches.
+2 = 78 min. (Y:58)

## Slide 6: Example of a Memory Chip
24-pin dual in-line package: 222  4-bit = 16Mibit memory
22-bit address is divided into
  11-bit row address
  11-bit column address
  Interleaved on same address lines
1
2
3
4
5
6
7
8
9
10
11
12
24
23
22
21
20
19
18
17
16
15
14
13
A4
A5
A6
A7
A8
A9
D3
D4
CAS
OE
Vss
Vss
A0
A1
A2
A3
A10
D1
D2
RAS
WE
Vcc
Vcc
NC
Legend
Ai
CAS
Dj
NC
OE
RAS
WE
Address bit i
Column address strobe
Data bit j
No connection
Output enable
Row address strobe
Write enable

## Slide 7: Typical Memory Structure
Row decoder
  Select row to read/write
Column decoder
  Select column to read/write
Cell Matrix
  2D array of tiny memory cells
Sense/Write amplifiers
  Sense & amplify data on read
  Drive bit line with data in on write
Same data lines are used for data in/out
Row address
r
. . .
2r × 2c × m bits
Cell Matrix
Row Decoder
Sense/write amplifiers
Column Decoder
. . .
Column address
c
Data
Row Latch 2c × m bits
m

## Slide 8: DRAM Operation
Row Access (RAS)
  Latch and decode row address to enable addressed row
  Small change in voltage detected by sense amplifiers
  Latch whole row of bits
  Sense amplifiers drive bit lines to recharge storage cells
Column Access (CAS) read and write operation
  Latch and decode column address to select m bits
  m = 4, 8, 16, or 32 bits depending on the DRAM package
  On read, send latched bits out to chip pins
  On write, charge storage cells to required value
  Can perform multiple column accesses to same row (burst mode)

## Slide 9: Burst Mode Operation
Used for Block Transfer
  Row address is latched and decoded
  A read operation causes ALL cells in a selected row to be read
  Selected row is latched internally inside the DRAM chip
  Column address is latched and decoded
  Selected column data is placed in the data output register
  Column address is incremented automatically
  Multiple data items are read depending on the block length
Fast transfer of blocks between main memory and cache
Fast transfer of pages between main memory and disk

## Slide 10: SDRAM and DDR SDRAM
SDRAM is Synchronous Dynamic RAM
  Added clock to DRAM interface
SDRAM is synchronous with the system clock
  Older DRAM technologies were asynchronous
  As system bus clock improved, SDRAM delivered higher performance than asynchronous DRAM
DDR is Double Data Rate SDRAM
  Like SDRAM, DDR is synchronous with the system clock, but the difference is that DDR reads data on both the rising and falling edges of the clock signal

## Slide 11: Memory Modules
Memory Rank: Set of DRAM chips accessed in parallel
  Same Chip Select (CS) and Command (CMD)
  Same address, but different data lines
  Increases memory capacity and bandwidth
  Example: 64-bit data bus using 4 × 16-bit DRAM chips
CLK
CMD
Address
Data
CS
. . .
Data width = p × m bits
. .
m
m
CLK
CMD
Address
Data
CS
CLK
CMD
Address
Data
CS

## Slide 12: Trends in DRAM
Year | Memory Standard | Chip Capacity (Mibit) | Bus Clock (MHz) | Data Rate (MT/s) | Peak Bandwidth (MB/s) | Total latency to a new row / column
1996 | SDRAM | 64-128 | 100-166 | 100-166 | 800-1333 | 60 ns
2000 | DDR | 256-512 | 100-200 | 200-400 | 1600-3200 | 55 ns
2004 | DDR2 | 512-2048 | 200-400 | 400-800 | 3200-6400 | 50 ns
2010 | DDR3 | 2048-8192 | 400-800 | 800-1600 | 6400-12800 | 40 ns
2014 | DDR4 | 8192-32768 | 800-1600 | 1600-3200 | 12800-25600 | 35 ns
Memory chip capacity: 1 Mibit = 220 bits, 1 Gibit = 230 bits
Data Rate = Millions of Transfers per second (MT/s)
Data Rate = 2 × Bus Clock for DDR, DDR2, DDR3, DDR4
1 Transfer = 8 bytes of data  Bandwidth = MT/s × 8 bytes

## Slide 13: Memory Latency versus Bandwidth
Memory Latency
  Elapsed time between sending address and receiving data
  Measured in nanoseconds
  The total latency to a new row/column is the time between opening a new row of memory and accessing a column within it.
  Reduced from 60 ns to 35 ns (between 1996 and 2016)
  Improvement in memory latency is less than 2X (1996 to 2016)
Memory Bandwidth
  Rate at which data is transferred between memory and CPU
  Bandwidth is measured as millions of Bytes per second
  Increased from 800 to 25600 MBytes/sec (between 1996 and 2016)
  Improvement in memory bandwidth is 32X (1996 to 2016)

## Slide 14: DRAM Refresh Cycles
Time
Threshold
voltage
0 Stored
1 Written
Refreshed
Refreshed
Refreshed
Refresh Cycle
Voltage
for 1
Voltage
for 0
Refresh cycle is about tens of milliseconds
Refreshing is done for the entire memory
Each row is read and written back to restore the charge
Some of the memory bandwidth is lost to refresh cycles

## Slide 15: Next . . .
Random Access Memory and its Structure
Memory Hierarchy and the need for Cache Memory
The Basics of Caches
Cache Performance and Memory Stall Cycles
Improving Cache Performance
Multilevel Caches

## Slide 16: Processor-Memory Performance Gap
1980 – No cache in microprocessor
1995 – Two-level cache on microprocessor
CPU Performance: 55% per year, slowing down after 2004
Performance Gap
DRAM: 7% per year

## Slide 17: The Need for Cache Memory
Widening speed gap between CPU and main memory
  Processor operation takes less than 1 ns
  Main memory requires more than 50 ns to access
Each instruction involves at least one memory access
  One memory access to fetch the instruction
  A second memory access for load and store instructions
Memory bandwidth limits the instruction execution rate
Cache memory can help bridge the CPU-memory gap
Cache memory is small in size but fast

## Slide 18: Typical Memory Hierarchy
Registers are at the top of the hierarchy
  Typical size < 1 KB
  Access time < 0.5 ns
Level 1 Cache (8 – 64 KiB)
  Access time: 1 ns
L2 Cache (1 MiB – 8 MiB)
  Access time: 3 – 10 ns
Main Memory (8 – 32 GiB)
  Access time: 40 – 50 ns
Disk Storage (> 200 GB)
  Access time: 5 – 10 ms
Microprocessor
Registers
Main Memory
Magnetic or Flash Disk
Memory Bus
I/O Bus
Faster
Bigger
L1 Cache
L2 Cache

## Slide 19: Principle of Locality of Reference
Programs access small portion of their address space
  At any time, only a small set of instructions & data is needed
Temporal Locality (in time)
  If an item is accessed, probably it will be accessed again soon
  Same loop instructions are fetched each iteration
  Same procedure may be called and executed many times
Spatial Locality (in space)
  Tendency to access contiguous instructions/data in memory
  Sequential execution of Instructions
  Traversing arrays element by element

## Slide 20: What is a Cache Memory ?
Small and fast (SRAM) memory technology
  Stores the subset of instructions & data currently being accessed
Used to reduce average access time to memory
Caches exploit temporal locality by …
  Keeping recently accessed data closer to the processor
Caches exploit spatial locality by …
  Moving blocks consisting of multiple contiguous words
Goal is to achieve
  Fast speed of cache memory access
  Balance the cost of the memory system

## Slide 21: Cache Memories in the Datapath
I-Cache miss or D-Cache miss causes pipeline to stall
ALU result
32
0
1
D-Cache
Address
Data_in
Data_out
32
R
D
Rd3
Data
Rd4
32
A
L
U
32
A
B
Rd2
clk
5
Rs
5
Rd
Rt
32
Register File
RA
RB
BusA
BusB
RW
BusW
0
1
Ext
0
2
3
1
0
2
3
1
I-Cache
Address
PC
Instruction
Instruction
Imm16
Interface to L2 Cache or Main Memory
I-Cache miss
D-Cache miss
Instruction Block
Data Block
Block Address
Block Address
Imm
1
0
0
2
1

## Slide 22: Almost Everything is a Cache !
In computer architecture, almost everything is a cache!
Registers: a cache on variables – software managed
First-level cache: a cache on second-level cache
Second-level cache: a cache on memory (or L3 cache)
Memory: a cache on hard disk
  Stores recent programs and their data
  Hard disk can be viewed as an extension to main memory
Branch target and prediction buffer
  Cache on branch target and prediction information

## Slide 23: Next . . .
Random Access Memory and its Structure
Memory Hierarchy and the need for Cache Memory
The Basics of Caches
Cache Performance and Memory Stall Cycles
Improving Cache Performance
Multilevel Caches

## Slide 24: Four Basic Questions on Caches
Q1: Where can a block be placed in a cache?
  Block placement
  Direct Mapped, Set Associative, Fully Associative
Q2: How is a block found in a cache?
  Block identification
  Block address, tag, index
Q3: Which block should be replaced on a cache miss?
  Block replacement
  FIFO, Random, LRU
Q4: What happens on a write?
  Write strategy
  Write Back or Write Through cache (with Write Buffer)

## Slide 25: Inside a Cache Memory
Processor
Cache
Memory
Main
Memory
Address
Data
Address
Data
Cache Block (or Cache Line)
  Unit of data transfer between main memory and a cache
  Large block size  Less tag overhead + Burst transfer from DRAM
  Typically, cache block size = 64 bytes in recent caches
Address Tag 0
Address Tag 1
Tag N – 1
Cache Block 0
Cache Block 1
Cache Block N – 1
N Cache Blocks
Tags identify
blocks in
the cache
. . .
. . .

## Slide 26: Block Placement: Direct Mapped
Block: unit of data transfer between cache and memory
Direct Mapped Cache:
  A block can be placed in exactly one location in the cache
000
001
010
011
100
101
110
111
00000
00001
00010
00011
00100
00101
00110
00111
01000
01001
01010
01011
01100
01101
01110
01111
10000
10001
10010
10011
10100
10101
10110
10111
11000
11001
11010
11011
11100
11101
11110
11111
In this example:
Cache index =
least significant 3 bits of Block address
Cache
Main
Memory

## Slide 27: Direct-Mapped Cache
A memory address is divided into
  Block address: identifies block in memory
  Block offset: to access bytes within a block
A block address is further divided into
  Index: used for direct cache access
  Tag: most-significant bits of block address
  Index = Block Address mod Cache Blocks
Tag must be stored also inside cache
  For block identification
A valid bit is also required to indicate
  Whether a cache block is valid or not
V
Tag
Block Data
=
Hit
Data
Tag
Index
offset
Block Address

## Slide 28: Direct Mapped Cache – cont’d
Cache hit: block is stored inside cache
  Index is used to access cache block
  Address tag is compared against stored tag
  If equal and cache block is valid then hit
  Otherwise: cache miss
If number of cache blocks is 2n
  n bits are used for the cache index
If number of bytes in a block is 2b
  b bits are used for the block offset
If 32 bits are used for an address
  32 – n – b bits are used for the tag
Cache data size = 2n+b bytes
V
Tag
Block Data
=
Hit
Data
Tag
Index
offset
Block Address

## Slide 29: Mapping an Address to a Cache Block
Example
  Consider a direct-mapped cache with 256 blocks
  Block size = 16 bytes
  Compute tag, index, and byte offset of address: 0x01FFF8AC
Solution
  32-bit address is divided into:
    4-bit byte offset field, because block size = 24 = 16 bytes
    8-bit cache index, because there are 28 = 256 blocks in cache
    20-bit tag field
  Byte offset = 0xC = 12 (least significant 4 bits of address)
  Cache index = 0x8A = 138 (next lower 8 bits of address)
  Tag = 0x01FFF (upper 20 bits of address)
Tag
Index
offset
4
8
20
Block Address

## Slide 30: Example on Cache Placement & Misses
Consider a small direct-mapped cache with 32 blocks
  Cache is initially empty, Block size = 16 bytes
  The following memory addresses (in decimal) are referenced:
  1000, 1004, 1008, 2548, 2552, 2556.
  Map addresses to cache blocks and indicate whether hit or miss
Solution:
  1000 = 0x3E8 cache index = 0x1E Miss (first access)
  1004 = 0x3EC cache index = 0x1E Hit
  1008 = 0x3F0 cache index = 0x1F Miss (first access)
  2548 = 0x9F4 cache index = 0x1F Miss (different tag)
  2552 = 0x9F8 cache index = 0x1F Hit
  2556 = 0x9FC cache index = 0x1F Hit
Tag
Index
offset
4
5
23

## Slide 31: Fully Associative Cache
A block can be placed anywhere in cache  no indexing
If m blocks exist then
  m comparators are needed to match tag
  Cache data size = m  2b bytes
m-way associative
Address
Tag
offset
Data
Hit
=
=
=
=
V
Tag
Block Data
V
Tag
Block Data
V
Tag
Block Data
V
Tag
Block Data
mux

## Slide 32: Set-Associative Cache
A set is a group of blocks that can be indexed
A block is first mapped onto a set
  Set index = Block address mod Number of sets in cache
If there are m blocks in a set (m-way set associative) then
  m tags are checked in parallel using m comparators
If 2n sets exist then set index consists of n bits
Cache data size = m  2n+b bytes (with 2b bytes per block)
  Without counting tags and valid bits
A direct-mapped cache has one block per set (m = 1)
A fully-associative cache has one set (2n = 1 or n = 0)

## Slide 33: Set-Associative Cache Diagram
m-way set-associative
V
Tag
Block Data
V
Tag
Block Data
V
Tag
Block Data
V
Tag
Block Data
Address
Tag
Index
offset
Data
=
=
=
=
mux
Hit

## Slide 34: Write Policy
Write Through:
  Writes update cache and lower-level memory
  Cache control bit: only a Valid bit is needed
  Memory always has latest data, which simplifies data coherency
  Can always discard cached data when a block is replaced
Write Back:
  Writes update cache only
  Cache control bits: Valid and Modified bits are required
  Modified cached data is written back to memory when replaced
  Multiple writes to a cache block require only one write to memory
  Uses less memory bandwidth than write-through and less power
  However, more complex to implement than write through

## Slide 35: What Happens on a Cache Miss?
Cache sends a miss signal to stall the processor
Decide which cache block to allocate/replace
  One choice only when the cache is directly mapped
  Multiple choices for set-associative or fully-associative cache
Transfer the block from lower level memory to this cache
  Set the valid bit and the tag field from the upper address bits
If block to be replaced is modified then write it back
  Modified block is written back to memory
  Otherwise, block to be replaced can be simply discarded
Restart the instruction that caused the cache miss
Miss Penalty: clock cycles to process a cache miss

## Slide 36: Replacement Policy
Which block to be replaced on a cache miss?
No selection alternatives for direct-mapped caches
m blocks per set to choose from for associative caches
Random replacement
  Candidate blocks are randomly selected
  One counter for all sets (0 to m – 1): incremented on every cycle
  On a cache miss replace block specified by counter
First In First Out (FIFO) replacement
  Replace oldest block in set
  One counter per set (0 to m – 1): specifies oldest block to replace
  Counter is incremented on a cache miss

## Slide 37: Replacement Policy – cont’d
Least Recently Used (LRU)
  Replace block that has been unused for the longest time
  Order blocks within a set from least to most recently used
  Update ordering of blocks on each cache hit
  With m blocks per set, there are m! possible permutations
Pure LRU is too costly to implement when m > 2
  m = 2, there are 2 permutations only (a single bit is needed)
  m = 4, there are 4! = 24 possible permutations
  LRU approximation is used in practice
For large m > 4,
Random replacement can be as effective as LRU

## Slide 38: Next . . .
Random Access Memory and its Structure
Memory Hierarchy and the need for Cache Memory
The Basics of Caches
Cache Performance and Memory Stall Cycles
Improving Cache Performance
Multilevel Caches

## Slide 39: Hit Rate and Miss Rate
Hit Rate = Hits / (Hits + Misses)
Miss Rate = Misses / (Hits + Misses)
I-Cache Miss Rate = Miss rate in the Instruction Cache
D-Cache Miss Rate = Miss rate in the Data Cache
Example:
  Out of 1000 instructions fetched, 150 missed in the I-Cache
  25% are load-store instructions, 50 missed in the D-Cache
  What are the I-cache and D-cache miss rates?
I-Cache Miss Rate = 150 / 1000 = 15%
D-Cache Miss Rate = 50 / (25% × 1000) = 50 / 250 = 20%

## Slide 40: Memory Stall Cycles
The processor stalls on a Cache miss
  When fetching instructions from the Instruction Cache (I-cache)
  When loading or storing data into the Data Cache (D-cache)
Memory stall cycles = Combined Misses  Miss Penalty
Miss Penalty: clock cycles to process a cache miss
Combined Misses = I-Cache Misses + D-Cache Misses
I-Cache Misses = I-Count × I-Cache Miss Rate
D-Cache Misses = LS-Count × D-Cache Miss Rate
LS-Count (Load & Store) = I-Count × LS Frequency
Cache misses are often reported per thousand instructions

## Slide 41: Memory Stall Cycles Per Instruction
Memory Stall Cycles Per Instruction =
Combined Misses Per Instruction × Miss Penalty
Miss Penalty is assumed equal for I-cache & D-cache
Miss Penalty is assumed equal for Load and Store
Combined Misses Per Instruction =
I-Cache Miss Rate + LS Frequency × D-Cache Miss Rate
Therefore, Memory Stall Cycles Per Instruction =
I-Cache Miss Rate × Miss Penalty +
LS Frequency × D-Cache Miss Rate × Miss Penalty

## Slide 42: Example on Memory Stall Cycles
Consider a program with the given characteristics
  Instruction count (I-Count) = 106 instructions
  30% of instructions are loads and stores
  D-cache miss rate is 5% and I-cache miss rate is 1%
  Miss penalty is 100 clock cycles for instruction and data caches
  Compute combined misses per instruction and memory stall cycles
Combined misses per instruction in I-Cache and D-Cache
  1% + 30%  5% = 0.025 combined misses per instruction
  Equal to 25 misses per 1000 instructions
Memory stall cycles
  0.025  100 (miss penalty) = 2.5 stall cycles per instruction
  Total memory stall cycles = 106  2.5 = 2,500,000

## Slide 43: CPU Time with Memory Stall Cycles
CPIPerfectCache = CPI for ideal cache (no cache misses)
CPIMemoryStalls = CPI in the presence of memory stalls
Memory stall cycles increase the CPI
CPU Time = I-Count × CPIMemoryStalls × Clock Cycle
CPIMemoryStalls = CPIPerfectCache + Mem Stalls per Instruction

## Slide 44: Example on CPI with Memory Stalls
A processor has CPI of 1.5 without any memory stalls
  Cache miss rate is 2% for instruction and 5% for data
  20% of instructions are loads and stores
  Cache miss penalty is 100 clock cycles for I-cache and D-cache
What is the impact on the CPI?
Answer:
Mem Stalls per Instruction =
CPIMemoryStalls =
CPIMemoryStalls / CPIPerfectCache =
Processor is 3 times slower due to memory stall cycles
Instruction
data
0.02×100 + 0.2×0.05×100 = 3
1.5 + 3 = 4.5 cycles per instruction
4.5 / 1.5 = 3

## Slide 45: Average Memory Access Time
Average Memory Access Time (AMAT)
AMAT = Hit time + Miss rate × Miss penalty
Time to access a cache for both hits and misses
Example: Find the AMAT for a cache with
  Cache access time (Hit time) of 1 cycle = 2 ns
  Miss penalty of 20 clock cycles
  Miss rate of 0.05 per access
Solution:
  AMAT = 1 + 0.05 × 20 = 2 cycles = 4 ns
  Without the cache, AMAT will be equal to Miss penalty = 20 cycles

## Slide 46: Next . . .
Random Access Memory and its Structure
Memory Hierarchy and the need for Cache Memory
The Basics of Caches
Cache Performance and Memory Stall Cycles
Improving Cache Performance
Multilevel Caches

## Slide 47: Improving Cache Performance
Average Memory Access Time (AMAT)
AMAT = Hit time + Miss rate * Miss penalty
Used as a framework for optimizations
Reduce the Hit time
  Small and simple caches
Reduce the Miss Rate
  Larger cache size, higher associativity, and larger block size
Reduce the Miss Penalty
  Multilevel caches

## Slide 48: Small and Simple Caches
Hit time is critical: affects the processor clock cycle
  Fast clock rate demands small and simple L1 cache designs
Small cache reduces the indexing time and hit time
  Indexing a cache represents a time consuming portion
  Tag comparison also adds to this hit time
Direct-mapped overlaps tag check with data transfer
  Associative cache uses additional mux and increases hit time
Size of L1 caches has not increased much
  L1 caches are the same size on Alpha 21264 and 21364
  Same also on UltraSparc II and III, AMD K6 and Athlon
  Reduced from 16 KB in Pentium III to 8 KB in Pentium 4!

## Slide 49: Classifying Misses – Three Cs
Conditions under which misses occur
Compulsory: program starts with no block in cache
  Also called cold start misses
  Misses that would occur even if a cache has infinite size
Capacity: misses happen because cache size is finite
  Blocks are replaced and then later retrieved
  Misses that would occur in a fully associative cache of a finite size
Conflict: misses happen because of limited associativity
  Limited number of blocks per set
  Non-optimal replacement algorithm

## Slide 50: Classifying Misses – cont’d
Compulsory misses are independent of cache size
  Very small for long-running programs
Conflict misses decrease as associativity increases
  Data were collected using LRU replacement
Capacity misses decrease as capacity increases
Miss Rate
0
2%
4%
6%
8%
10%
12%
14%
1
2
4
8
16
32
64
128 KB
1-way
2-way
4-way
8-way
Capacity
Compulsory

## Slide 51: Larger Size and Higher Associativity
Increasing cache size reduces capacity misses
It also reduces conflict misses
  Larger cache size spreads out references to more blocks
Drawbacks: longer hit time and higher cost
Larger caches are especially popular as 2nd level caches
Higher associativity also improves miss rates
  Eight-way set associative is as effective as a fully associative

## Slide 52: Larger Block Size
Simplest way to reduce miss rate is to increase block size
However, it increases conflict misses if cache is small
Block Size (bytes)
Miss Rate
0%
5%
10%
15%
20%
25%
16
32
64
128
256
1K
4K
16K
64K
256K
Increased Conflict Misses
Reduced Compulsory Misses
64-byte blocks are common in L1 caches
128-byte block are common in L2 caches

## Slide 53: Multilevel Caches
Top level cache should be kept small to
  Keep pace with processor speed
Adding another cache level
  Can reduce the memory gap
  Can reduce memory bus loading
Local miss rate
  Number of misses in a cache / Memory accesses to this cache
  Miss RateL1 for L1 cache, and Miss RateL2 for L2 cache
Global miss rate
Number of misses in a cache / Memory accesses generated by CPU
Miss RateL1 for L1 cache, and Miss RateL1  Miss RateL2 for L2 cache
Unified L2 Cache
I-Cache
D-Cache
Main Memory

## Slide 54: Power 7 On-Chip Caches [IBM 2010]
32KB I-Cache/core
32KB D-Cache/core
3-cycle latency
256KB Unified
L2 Cache/core
8-cycle latency
32MB Unified
Shared L3 Cache
Embedded DRAM
25-cycle latency
to local slice

## Slide 55: Multilevel Cache Policies
Multilevel Inclusion
  L1 cache data is always present in L2 cache
  A miss in L1, but a hit in L2 copies block from L2 to L1
  A miss in L1 and L2 brings a block into L1 and L2
  A write in L1 causes data to be written in L1 and L2
  Typically, write-through policy is used from L1 to L2
  Typically, write-back policy is used from L2 to main memory
    To reduce traffic on the memory bus
  A replacement or invalidation in L2 must be propagated to L1

## Slide 56: Multilevel Cache Policies – cont’d
Multilevel exclusion
  L1 data is never found in L2 cache – Prevents wasting space
  Cache miss in L1, but a hit in L2 results in a swap of blocks
  Cache miss in both L1 and L2 brings the block into L1 only
  Block replaced in L1 is moved into L2
  Example: AMD Athlon
Same or different block size in L1 and L2 caches
  Choosing a larger block size in L2 can improve performance
  However different block sizes complicates implementation
  Pentium 4 has 64-byte blocks in L1 and 128-byte blocks in L2